## Slide 1: Latest Update DPACC Use-cases
https://docs.google.com/document/d/1eu2489SYeVL180ZzjnagrXTUM1Qh37GKs6N6rRYDVNM/edit
2/18/2016

## Slide 2: Table of Contents
Introduction
Acceleration Models: Lookaside Model, Offload Model (Inline Model), External Model (Data Path Offload Model)
Virtualized Acceleration Interfaces: Passthrough-based Acceleration & Virtio-based Acceleration
  Virtio-lookaside Acceleration & virtio-inline acceleration
Targeting Applications: SmallCell Gateway. IPSec between vRAN and vEPC, VRAN
  IPsec Packet Processing Acceleration
  NFVI Packet Processing Acceleration
  PDCP Packet Processing Acceleration
Use-cases
  IPsec Look Aside Accelerator
  NFVI Packet Processing Offload Accelerator
  Combined NFVI Inline and IPsec LA Accelerator
  NFVI and IPsec Offload Accelerator
  PDCP Offload Accelerator
vRAN application description refined.
Update on the figures to align with dpacc arch.

## Slide 3: Update Summary
Refine vRAN application statement
  Remove text statements from the figure
  Add LTE stack figure to illustrate various accelerators involved
  Add more accelerators to lookaside/inline model examples
Starting working on the usecase figures
  Remove irrelevant technical details
  Be aligned with dpacc arch

## Slide 4
UE
Backhaul Network
Core Network
Internet
Fronthaul Network
RRU +
Partial baseband function(optional)
Radio Stack
Virtual RAN
…
…
…
…
Targeting applications: virtual RAN (vRAN)
eNB VM
eNB VM
eNB VM
Compute nodes
Host Linux (vSwitch Acceleration + vRAN acceleration)
L2/L3 VM
L1 VM
vRAN VM
There are two main vRAN VM design schemes:
  eNB VM: all the radio access network protocol functions (including L1, L2, L3) are in eNB VM.
  L2/L3 VM and L1 VM: according to the wireless features, different layers of radio access network protocol are in different VMs
vRAN accelerator
vRAN accelerator: vRAN accelerator mainly refers to compute-intensive functions acceleration, based on the evaluation of LTE protocol stack, it includes PDCP ciphering/deciphering, PDCP Robust Header Compression, channel encoding/decoding and FFT/iFFT, etc.
Two classes of vRAN accelerator:
  Radio load dependent accelerator, such as PCDP accelerator, channel encoding/decoding accelerator
  Radio load independent accelerator, such as FFT/iFFT accelerator

## Slide 5: Targeting applications vRAN (LTE Stack illustration & Accelerator models)
Look aside
Look aside
Inline (offload)
Two types of look-aside accelerator identified
Added into Section 2.1 as examples;
Clarifications added in Section 4.3.
One types of offload accelerator identified
Added into Section 2.2 as examples;
Clarifications added in Section 4.3.

## Slide 6: Update Summary
Refine vRAN application statement
  Remove text statements from the figure
  Add LTE stack figure to illustrate various accelerators involved
  Add more accelerators to lookaside/inline model examples
Starting working on the usecase figures
  Remove irrelevant technical details
  Be aligned with dpacc arch

## Slide 7: Look Aside Accelerator
SAL
SW Accelerator
SAL
sio
virtio-la frontend
hio
HW Accelerator (Crypto)
host
guest
device
virtio-la backend
vHost-user
VNF - LA Application
SAL
HW (NIC)
sio
virtio-net frontend
hio
virtio-net backend
SAL
HW (NIC)
sio
virtio-net frontend
hio
virtio-net backend
①
②
③
③
④
⑤
Notes: This view is attempting to how the DPACC layer and configuration can be designed by the developer to give his application the best accelerated performance.
In this picture having a software acceleration layer in the host would provide the best performance and flexibility for a VNF application.

## Slide 8: PDCP Look Aside Accelerator
SAL
SW Accelerator
SAL
sio
virtio-la-pdcp frontend
hio
HW Accelerator (Crypto)
host
guest
device
virtio-la-pdcp backend + vHost-user
VNF - PDCP Application
SAL
HW (NIC)
sio
virtio-net frontend
hio
virtio-net backend
Backhaul Processing GTPU/IPSec/QoS
Backplane Processing RLC/MAC/PHY
EPC
Downlink
Uplink
SAL
HW (NIC)
sio
virtio-net frontend
hio
virtio-net backend
UE
Notes: This view is attempting to how the DPACC layer and configuration can be designed by the developer to give his application the best accelerated performance.
In this picture having a software acceleration layer in the host would provide the best performance and flexibility for a VNF application.

## Slide 9: Todos
Address remaining issues online
  Keep on working on other usecase figures
Call for review and feedback
Anything missing?