## Slide 1
DPACC
IPSEC Performance Testing
Srinivasa Addepalli (Intel)
Lingli Deng (China Mobile)
Bose Perumal (Dell)

## Slide 2
Use case : IPSec between vRAN and vEPC
eNB VM
eNB VM
IPSec VM
eNB VM
IPSec VM
vRAN Sites
Wireless
IPSec
IPSec
SGW
SGW
PGW
PGW
PGW
Firewall
IPS/DPI
IPS/DPI
HSS
MME
PCRF
AAA
EPC
IPSEC Tunnels
Openstack VIM
Compute nodes
Compute nodes
Host Linux (vSwitch acceleration + IPSEC-LA acceleration)
Host Linux (vSwitch Acceleration + IPSEC-LA acceleration)
Openstack VIM
Orchestrator

## Slide 3
Test Setup
IPSec VM
IPSec VM
IPSEC Tunnels
Host Linux (vSwitch acceleration + IPSEC-LA acceleration)
Host Linux (vSwitch Acceleration + IPSEC-LA acceleration)
Horizon Dashboard
Openstack VIM & VPN-as-a-Service
IXIA/Spirent
Test Controller
Bring Up IPSec VMs using NOVA
Configure IPSec Policies using VPN-as-a-Service
Configure IXIA to start the traffic and measure the returned traffic
Encrypted Traffic
Clear Traffic

## Slide 4
Use case : IPSec GW for small cells
UE
SmallCell
BackhaulNetwork
SmallCell
GW
EPC
Internet
SmGW
Signaling Routing: selects a proper MME for an attaching UE.
Signaling Pooling: pools the interfaces to MME for a large group of small cells.
Optional
SeGW
Authentication: realize mutual authentication between small cell and GW.
Security Protection: establish IPSec tunnels between small cell and GW.
QoS Inheritance: copies the inner IP ToS/DSCP tags onto the outerIP header during encapsulation.
Host Linux (vSwitch Acceleration + IPSEC-LA acceleration)
Compute node
SeGW
SmGW

## Slide 5
Test Setup
SeGW VM
SeGW
VM
IPSEC Tunnels
Host Linux (vSwitch acceleration + IPSEC-LA acceleration)
Host Linux (vSwitch Acceleration + IPSEC-LA acceleration)
Horizon Dashboard
Openstack VIM & VPN-as-a-Service
IXIA/Spirent
Test Controller
Bring Up IPSec VMs using NOVA
Configure IPSec Policies using VPN-as-a-Service
Configure IXIA to start the traffic and measure the returned traffic
Encrypted Traffic
Clear Traffic
SeGW emulated eNBs

## Slide 6: Performance Expectations on EPC SecGw (Based on inputs from China Mobile)
Performance Parameters | Low End | Medium End | High end
Bandwidth | 10Gbps | 20Gbps | 40Gbps
Single Tunnel Bandwidth | 4Gbps | 4Gbps | 4Gbps
IPSec Tunnels | 5000 | 20000 | 40000
Tunnel Setup Rate/second | 1000 | 2000 | 4000
AES-128 and SHA-1, AES-256 and SHA-2 algorithm
Certificate Authentication (RSA certificates with 2048 key size) on both sides, IKEv2
Packet Size : 512 bytes. Also take measurements for 1024, 1400, 2048, 4K packet sizes

## Slide 7: Performance Measurements
Packet Size | Algorithm | Tunnels | Number of cores dedicated to Guest | Number of cores dedicated to Host | Burstiness | Throughput | Jitter (Min/Max/Avg) | Latency (Min, Max, Avg) | % of out-of-order packets on the flows
64 512 1K 2K 4K | Tunnel Mode, AES-128, SHA-1 Tunnel Mode AES-128, SHA-2 Transport Mode AES-128 and SHA-1 Tunnel mode AES-GCM Tunnel mode AES-256 and SHA-2 | 1 512 5000 20000 40000 | 1 2 4 8 16 | 1 2 4 8 16 | 1 10 |  |  |  | 
Measurement for various combination of above need to be recorded.
Packet Size | Algorithm | Tunnels | Number of cores dedicated to Guest | Number of cores dedicated to Host | Burstiness | Throughput | Jitter (Min/Max/Avg) | Latency (Min, Max, Avg) | % of out-of-order packets on the flows
512 4K | Tunnel Mode, AES-128, SHA-1 | 1 512 | 2 | 2 | 1 |  |  |  | 
Minimal combinations

## Slide 8: DUT - Config
DUT Instantiation
  OpenStack Commands
    ?
Interface Config
IPSec Config Commands
    ?