## Slide 1
Platform Performance Acceleration
Keith Wiles (Intel)
Bob Monkman (ARM)
v11 (2015/05/02)

## Slide 2
DPACC Overview
Data Plane Acceleration for NFV
Keith Wiles
Principle Engineer @ Intel Corporation

## Slide 3: Session Agenda
DPACC: Data Plane Acceleration
  A high level view of how acceleration is added to NFV
Project Plan
  Current timeline of the project phases
Goals for the project
Acceleration Layers and Examples
Summary of DPACC

## Slide 4
Data Plane Acceleration Overview
What are the goals of DPACC?
Identify NFV use cases to illustrate Data Plane Acceleration
Provide a clean standard solution for VNF deployments on ‘Standard High Volume’ (SHV) servers
  Create a common framework from which all VNFs can utilize
  Agree on the method(s) to move control/data between guest (VNF) and host with acceleration support
  Allow for orchestration layers to be able to manage and configure the HW/SW accelerators easily
  Suggest a solution(s) to OPNFV as a document and PoC
DPACC: Data Plane Acceleration

## Slide 5: Early Project Phased Plan
Phase 1: (by 2015Q2)
  document typical VNF use-cases and high-level requirements
    Generic functional abstraction for high performance data plane and acceleration functions, including hardware and software acceleration
  Identify the potential extensions across various NFV interfaces
  Evaluate current state-of-art solutions from open-source upstream projects according to identified requirements and targeted framework
Phase 2: (by 2015Q4)
  Specify detailed framework/API design/choice and document test cases for selected use-cases;
  Provide open source implementation for both the framework and test tools
  Coordinate integrated testing and release testing results
  Finalized interface specification
Notes: Phase 1 is to be completed this year in Q2.
The deliverables for Phase 1 is to define VNF use-cases plus high level requirements for HW and SW acceleration functions.
Plus we need to identify open-source projects which will help us identify requirements and targeted frameworks.
Phase 2 ending in Q4 of this year we need to define a framework and API for the use-cases we identified in Phase 1, plus provide open source implementations.
We also need to create test tools and release process to be able to finalize the API specifications.

## Slide 6
Data Plane Acceleration Goals (directly from Wiki)
The project is to specify a general framework for VNF Data Plane Acceleration (DPA or DPACC)
Including a common suite of abstract APIs at various OPNFV interfaces
Enable VNF portability and resource management across various underlying integrated SOCs and standard high volume servers (SHV), with/without hardware accelerators
It may desirable to design such DPA API framework to easily fit underneath existing prevalent APIs (e.g. sockets), as a design choice, for legacy designs
The framework should not dictate what APIs an application must use, rather recognizing the API abstraction is likely a layered approach and developers can decide which layer to access directly
DPACC: Goals
Notes: As a result of convergence of various traffic types and increasing data rates, the performance requirements (both in terms of bandwidth and real-time-ness) on data plane devices within network infrastructure have been growing at significantly higher rates than in the past.
As the traditional ‘bump-in-the-wire’ network functions evolve to a virtualized paradigm with NFV, the focus will be even higher to deliver high performance within very competitive cost envelopes. At the same time, application developers have, in some cases, taken advantage of various hardware and software acceleration capabilities, many of which are platform supplier dependent. There is a clear impetus to move away from proprietary data plane interfaces, in favor of more standardized interfaces to leveraging the data plane capability of underlying platforms – whether using specialized hardware accelerators or general purpose CPUs.
The goal of this project is to specify a general framework for VNF data plane acceleration (or DPA for short), including a common suite of abstract APIs at various OPNFV interfaces, to enable VNF portability and resource management across various underlying integrated SOCs that may include hardware accelerators or standard high volume (or SHV) server platforms that may include attached hardware accelerators. It may be desirable, as a design choice, in some cases, that such DPA API framework could easily fit underneath existing prevalent APIs (e.g. sockets) – mainly for legacy implementations even though they may not be most performance efficient. But this project should not seek to dictate what APIs an application must use, rather recognizing that API abstraction is likely a layered approach and developers can decide which layer to access directly, depending on the design choice for a given application usage.

## Slide 7: DPACC: Acceleration Layer for Guest (VM’s)
SAL: Software Acceleration Layer
  Provides a target abstraction for application software
g-API: Generic API for application portability (required)
  API as a standard application interface and is required
legacy-API: Legacy API for applications (Optional)
  The legacy-API layer is to help existing applications using APIs like sockets, libcrypto, …
s-API: APIs for utilizing an AC (APIs from the AC)
sio: software I/O interface
  e.g. VirtIO to the underlying SW/HW
  Enables binary compatibility with paravirtualized drivers
  Optional for hio-only requirements
g-drivers: General driver for each device type
  Implemented in software or the frontend to the hardware (may be different for different acceleration functions)
hio: Hardware I/O interface
  Some type of pass-through design with support for virtualization (e.g. SR-IOV, SoC-specific interfaces, etc.) Optional for sio-only deployments
Acceleration Core (AC)
e.g. DPDK, ODP or another acceleration implementation
sio + VirtIO
hio
legacy-API
Buffer and memory mgnt, rings/queues, ingress/egress scheduling, tasks, pipeline, …
Software Acceleration Layer (SAL)
g-drivers
for (paravirtualized)
SW/HW-funcs
s-API
Acceleration Management Layer
VNF Application
Virtual Machine or Guest
g-API**
  ** If s-API is AC specific APIs and cannot provide portability across platforms, then the g-API is mandatory to ensure portability

## Slide 8: DPACC: Acceleration Layer for Host (Hypervisor)
SAL: Software Acceleration Layer
  Provides an abstraction between SW and HW
sio-backend: backend of paravirtualized drivers
  vHost-user: User space based VirtIO interface
    optional for VM   host access
s-API: APIs for utilizing an AC (APIs from the AC)
g-drivers: General driver for each device type
  Implemented in software or the frontend to the hardware (may be different for different acceleration functions)
hio: Hardware I/O interface
  Non-virtualized, accessed only by host SAL
AC: Software/Hardware Acceleration Core
  e.g. DPDK, ODP or other acceleration implementation
SRL: Software Routing Layer (Optional layer for the host)
Open vSwitch (OVS) or vRouter
AML: Acceleration Management Layer
To be define for orchestration and spans more than the SAL
Acceleration Core (AC)
hio
sio-backend (optional vHost-user)
s-API
Acceleration Management Layer
Software Acceleration Layer (SAL)
Software Routing Layer (SRL)
Buffer and memory mgnt, rings/queues, ingress/egress scheduling, tasks, pipeline, …
g-drivers
SW-crypto or drivers for HW-crypto
VM 0
VM 2
VM 1
VM 3
VM 4
Notes: The sio-backend could be a set of paravirtualized drivers plus it can contain the implementation of the VirtIO backend call vHost-user.
The software routing layer (SRL) is here to manage routing or switching of packets to external or internal system. We need some type of SRL to give support of VM to VM communication without having leave the system as in the case of an external router or switch.
Possible SRL applications could be Open vSwitch or a vRouter design.
The AML layer is TBD and we expect this layer to interface to the orchestration layer to allow the orchestration layer to help manage the VNF applications.

## Slide 9: Usage: VNF Acceleration types
Showing two possible options:
Example A
  Legacy application using crypto lib via VirtIO to accelerate crypto operations in the host
  Crypto support is contained on the guest SAL maybe using external hardware
  VM to VM still missing, but can be supported by Host-SAL or Guest-SAL to external vSwitch accelerator
  vHost-user shown here (normally in the SAL) for sio+ access
  Host/sio+ layers are optional in some configurations
Example B
  Legacy application being agnostic to the encrypted traffic being handled in the host/accelerator
  Adding a SRL (vSwitch/vRouter) for VM to VM communication
  SRL implies it contains the vHost-user interface instead of SAL
  HW-Crypto or HW vSwitch at the device layer
  Host layer is optional in some configurations
+ Standard or enhanced backend VirtIO to vHost-user in the host SAL
host
guest
device
sio+
Accelerator
SAL
Legacy
Application
(crypto -agnostic)
Standard APIs
sio+
Accelerator
SAL
HW
Switch/Crypto
SRL
hio
A
B
hio
Application
hio
sio-backend + vHost-user
sio-backend + vHost-user
SAL
Crypto
Notes: Both options are attempting to show a number of options or layers a VNF could deploy in many different configurations.
Looking at A we can see a number of layers in the guest and host plus a couple of optional layers. In this example the guest can have crypto support in software or using a external crypto hardware via the hio interface.
The sio is optional in the cases where the guest does not require direct access to the host for any reason, but as the sio layer is normally present it can be used for management access to the guest.
If the guest does not require host support the host layer are optional. The host layer allows the guest to have better acceleration support without having to have a SAL layer in the guest.
Looking at B we have a legacy application which is crypto agnostic, which means it sends and receives packet in clear text format as the host layer is encrypting or decrypting the packets unbeknownst to the guest application. The guest has only the standard sio support, but is accelerated because we have a acceleration layer in the host.

## Slide 10: Usage: VNF Acceleration (e.g. crypto)
Showing a number of possible options:
Example A (non-hio packets have poor performance)
  VM with a SAL for direct access to external device
  The sio is optional for host access for management
  VM to VM support only supplied by vSwitch or external device
Example B
  Legacy application using crypto lib via VirtIO to accelerate crypto operations in the host
  VM to VM still missing, but can be supported by SAL to external vSwitch accelerator
Example C
  Legacy application being agnostic to the encrypted traffic being handled in the host/accelerator
  Adding a SRL (vSwitch/vRouter) for VM to VM communication
Example D
  Accelerated application using SAL in guest to access crypto accelerator directly
  Flexible vSwitch or vRouter support in SW or HW
  SAL allows for some/all crypto operations to be done in the guest on passed to the host for processing
Application
SAL
Crypto
sio*
hio
Accelerator
vSwitch
host
guest
device
Legacy
Application
Standard APIs
cryptolib
sio**
Accelerator
SAL
SW Crypto
Legacy
Application
(crypto -agnostic)
Standard APIs
sio**
Accelerator
SAL
HW Crypto
Accelerator
SAL
Crypto
Application
SAL
sio
hio
SRL
SRL
Crypto
hio
A
B
C
D
hio
Crypto
hio
vSwitch
* Standard VirtIO and Kernel based vHost, Kernel layer not shown
** Standard or enhanced VirtIO to vHost-user in the SAL

## Slide 11: NFV High Level View
Focus on one as a basic high level view:
Software Acceleration Layer is the software to hardware abstraction layer
Software Acceleration Layer makes possible additional services which can be controlled by the orchestration layer
sio-backend + vHost-user is normally in the SAL or SRL layer, but shown here to illustrate vHost in the host.
A SAL in the guest allows for the best performance selection
  Direct access to hardware acceleration via SR-IOV, SOC-specific interface or other pass-though
  Able to do software acceleration in the guest
SRL or HW vSwitch adds VM2VM routing or switching of packets
A SAL in the host gives scalability for non-accelerated VMs and/or native applications
Accelerator
SAL
Crypto
Application
SAL
sio
hio
SRL
Crypto
hio
HW vSwitch/Crypto
host
guest
device
sio-backend + vHost-user
Notes: This view is attempting to how the DPACC layer and configuration can be designed by the developer to give his application the best accelerated performance.
In this picture having a software acceleration layer in the host would provide the best performance and flexibility for a VNF application.

## Slide 12: Related Upstream Work Plan of DPACC
Enhancing VirtIO for better control and adding more device types:
Need to look at adding Crypto support to VirtIO as an acceleration feature
Needs to support legacy VirtIO API for backward compatibility as a requirement
Needs to support exporting VNF metadata needs for acceleration and orchestration
Enhance performance as a requirement for the solution
Enhancing Software Acceleration Layer:
Help locate/find hardware/software acceleration mechanisms for the VNFs
SAL acceleration must support a number of software and/or hardware accelerators
Help enhance support for orchestration layer along with the VIM for plumbing the data flows
Enhancing OpenStack for acceleration orchestration and management:
Acceleration resource lifecycle management is a requirement
Acceleration requirement description and orchestration is a requirement

## Slide 13
Thank you for Attending
Keith Wiles & Bob Monkman