## Slide 1
Platform Performance Acceleration
Keith Wiles (Intel)
Bob Monkman (ARM)

## Slide 2: Session Agenda
DPACC: Data Plane Acceleration
  A high level view of how acceleration is added to NFV
??

## Slide 3
DPACC Overview
Data Plane Acceleration for NFV
Keith Wiles
Principle Engineer @ Intel Corp

## Slide 4
Data Plane Acceleration Overview
What are the goals of DPACC?
Identify NFV use cases to illustrate Data Plane Acceleration and propose a solution
Agree on the method(s) to move control/data between guest (vNF) and host with acceleration support
Provide a clean standard solution for vNF deployments on ‘Standard High Volume’ (SHV) servers
Create a common framework from which all vNFs can utilize
Allow for orchestration layers to be able to manage and configure the compute node easily
Suggest a solution(s) to OPNFV as a document and PoC
DPACC: Data Plane Acceleration

## Slide 5: Early Project Phased Plan
Phase 1: (by 2015Q2)
  document typical VNF use-cases and high-level requirements
    Generic functional abstraction for high performance data plane and acceleration functions, including hardware and software acceleration
  Identify the potential extensions across various NFV interfaces
  Evaluate current state-of-art solutions from open-source upstream projects according to identified requirements and targeted framework.
Phase 2: (by 2015Q4)
  Specify detailed framework/API design/choice and document test cases for selected use-cases;
  Provide open source implementation for both the framework and test tools;
  Coordinate integrated testing and release testing results
  Finalized interface specification

## Slide 6
Data Plane Acceleration Goals (directly from Wiki)
The project is to specify a general framework for vNF Data Plane Acceleration (DPA or DPACC)
Including a common suite of abstract APIs at various OPNFV interfaces
Enable vNF portability and resource management across various underlying integrated SOCs and standard high volume servers (SHV), with/without hardware accelerators
It may desirable to design such DPA API framework to easily fit underneath existing prevalent APIs (e.g. sockets), as a design choice, for legacy designs
The framework should not dictate what APIs an application must use, rather recognizing the API abstraction is likely a layered approach and developers can decide which layer to access directly
DPACC: Goals
Notes: As a result of convergence of various traffic types and increasing data rates, the performance requirements (both in terms of bandwidth and real-time-ness) on data plane devices within network infrastructure have been growing at significantly higher rates than in the past. As the traditional ‘bump-in-the-wire’ network functions evolve to a virtualized paradigm with NFV, the focus will be even higher to deliver high performance within very competitive cost envelopes. At the same time, application developers have, in some cases, taken advantage of various hardware and software acceleration capabilities, many of which are platform supplier dependent. There is a clear impetus to move away from proprietary data plane interfaces, in favor of more standardized interfaces to leveraging the data plane capability of underlying platforms – whether using specialized hardware accelerators or general purpose CPUs.
The goal of this project is to specify a general framework for VNF data plane acceleration (or DPA for short), including a common suite of abstract APIs at various OPNFV interfaces, to enable VNF portability and resource management across various underlying integrated SOCs that may include hardware accelerators or standard high volume (or SHV) server platforms that may include attached hardware accelerators. It may be desirable, as a design choice, in some cases, that such DPA API framework could easily fit underneath existing prevalent APIs (e.g. sockets) – mainly for legacy implementations even though they may not be most performance efficient. But this project should not seek to dictate what APIs an application must use, rather recognizing that API abstraction is likely a layered approach and developers can decide which layer to access directly, depending on the design choice for a given application usage.

## Slide 7: DPACC: Acceleration Layer for Guest (VM’s)
SAL: Software Acceleration Layer
  Provides a target abstraction for application software
g-API: Generic API for applications (TBD or Optional)
  Layer for Application centric APIs, like sockets, libcrypto, …
  The g-API layer is TDB and may not be present in the final version
s-API: AC specific APIs
sio: software I/O interface
  e.g. VirtIO to the underlying SW/HW
  Enables binary compatibility
  Optional for hio-only requirements
g-drivers: General driver for each device type
  Implemented in software or the frontend to the hardware (may be different for different acceleration functions)
hio: Hardware I/O interface
  Some type of pass-through design with support for virtualization (e.g. SR-IOV, SoC-specific interfaces, etc.)
  Optional for sio-only deployments
AC: Acceleration Core
  e.g. DPDK, ODP or other acceleration implementation
Acceleration Core (AC)
sio
hio
g-API (TBD)
Buffer and memory mgnt, rings/queues, ingress/egress scheduling, tasks, pipeline, …
Software Acceleration Layer (SAL)
g-drivers
for (paravirtualized)
SW/HW-funcs
s-API
Acceleration Management Layer
vNF Application
Virtual Machine or Guest

## Slide 8: DPACC: Acceleration Layer for Host (Hypervisor)
SAL: Software Acceleration Layer
  Provides an abstraction between SW and HW
sio-backend: backend of paravirtualized drivers
vHost-user: User space based VirtIO interface
  optional for VM   host access
s-API: AC-specific APIs
g-drivers: General driver for each device type
  Implemented in software or the frontend to the hardware (may be different for different acceleration functions)
hio: Hardware I/O interface
  Non-virtualized, accessed only by host SAL
AC: Software/Hardware Acceleration Core
  e.g. DPDK, ODP or other acceleration implementation
SRL: Software Routing Layer (Optional layer for the host)
Open vSwitch (OVS) or vRouter
AML: Acceleration Management Layer
To be define for orchestration and spans more than the SAL
Acceleration Core (AC)
hio
sio-backend
s-API
Acceleration Management Layer
vHost-user
Software Acceleration Layer (SAL)
Software Routing Layer (SRL)
Buffer and memory mgnt, rings/queues, ingress/egress scheduling, tasks, pipeline, …
g-drivers
SW-crypto or drivers for HW-crypto
VM 0
VM 2
VM 1
VM 3
VM 3

## Slide 9: Usage: VNF Acceleration types
Showing a number of possible options:
Example A
  The standard method today using VirtIO and kernel vHost
  Performance is very poor due to kernel interaction
  VM to VM support only supplied by external device (ToR)
    Effects network utilization and performance
Example B
  Legacy application using crypto lib via VirtIO to accelerate crypto operations in the host
  VM to VM still missing, but can be supported by SAL to external vSwitch accelerator
  vHost-user shown here (normally in the SAL) for sio+ access
Example C
  Legacy application being agnostic to the encrypted traffic being handled in the host/accelerator
  Adding a SRL (vSwitch/vRouter) for VM to VM communication
  SRL implies it contains the vHost-user interface instead of SAL
Example D
  Accelerated application using SAL in guest to access crypto accelerator or vSwitch directly
  SAL allows for some/all crypto operations to be done in the guest on passed to the host for processing
* Standard VirtIO and Kernel based vHost, Kernel layer not shown
+ Standard or enhanced VirtIO to vHost-user in the SAL
sio*
Accelerator
host
guest
device
cryptolib
sio+
Accelerator
SAL
Legacy
Application
(crypto -agnostic)
Standard APIs
sio+
Accelerator
SAL
HW Crypto
Accelerator
Application
SAL
sio*
hio
SRL
Crypto
hio
A
B
C
D
hio
Legacy
Application
Standard APIs
Application
SAL
hio
vHost-user
HW Crypto

## Slide 10: Usage: VNF Acceleration (e.g. crypto)
Showing a number of possible options:
Example A (non-hio packets have poor performance)
  VM with a SAL for direct access to external device
  The sio is optional for host access for management
  VM to VM support only supplied by vSwitch or external device
Example B
  Legacy application using crypto lib via VirtIO to accelerate crypto operations in the host
  VM to VM still missing, but can be supported by SAL to external vSwitch accelerator
Example C
  Legacy application being agnostic to the encrypted traffic being handled in the host/accelerator
  Adding a SRL (vSwitch/vRouter) for VM to VM communication
Example D
  Accelerated application using SAL in guest to access crypto accelerator directly
  Flexible vSwitch or vRouter support in SW or HW
  SAL allows for some/all crypto operations to be done in the guest on passed to the host for processing
Application
SAL
Crypto
sio*
hio
Accelerator
vSwitch
host
guest
device
Legacy
Application
Standard APIs
cryptolib
sio**
Accelerator
SAL
SW Crypto
Legacy
Application
(crypto -agnostic)
Standard APIs
sio**
Accelerator
SAL
HW Crypto
Accelerator
SAL
Crypto
Application
SAL
sio
hio
SRL
SRL
Crypto
hio
A
B
C
D
hio
Crypto
hio
vSwitch
* Standard VirtIO and Kernel based vHost, Kernel layer not shown
** Standard or enhanced VirtIO to vHost-user in the SAL

## Slide 11: NFV High Level View (Continued)
Focus on ‘D” as a basic high level view:
Software Acceleration Layer is the software to hardware abstraction layer
Software Acceleration Layer makes possible additional services which can be controlled by the orchestration layer
A SAL in the guest allows for the best performance selection
  Direct access to hardware acceleration via SR-IOV, SOC-specific interface or other pass-though
  Able to do software acceleration in the guest
Software Routing Layer adds VM to VM routing or switching of packets
A SAL in the host gives scalability for non-accelerated VMs and/or native applications
D
Accelerator
SAL
Crypto
Application
SAL
sio
hio
SRL
Crypto
hio
vSwitch
host
guest
device

## Slide 12: Summary of DPACC
Enhancing VirtIO for better control and adding more device types:
Need to look at adding Crypto support to VirtIO as an acceleration feature
Needs to support legacy VirtIO API for backward compatibility as a requirement
Needs to support exporting the metadata needs of the vNF for acceleration and orchestration
Enhance performance as a requirement for the solution
Acceleration Layer enhancements:
Help locate/find hardware/software acceleration mechanisms for the vNFs
Help enhance support for orchestration layer along with the VIM for plumbing the data flows
vNF lifecycle management is a requirement
SAL acceleration must support a number of software accelerators as well as hardware accelerators