## Slide 1: HA Scenarios

## Slide 2: Service Availability Levels
 | Recovery Time | Customer Type | Recommendations
SAL 1 | 5 – 6 seconds | Network Operator Control Traffic Government/Regulatory Emergency Services | Redundant resources to be made available on-site to ensure fast recovery.
SAL32 | 10 – 15 seconds | Enterprise and/or large scale Customers Network Operators service traffic | Redundant resources to be available as a mix of on-site and off-site as appropriate. On-site resources to be utilized for recovery of real-time services. Off-site resources to be utilized for recovery of data services.
SAL 3 | 20 – 25 seconds | General Consumer Public and ISP Traffic | Redundant resources to be mostly available off-site. Real-time services should be recovered before data services
Source: ETSI GS NFV-REL 001 V1.1.1

## Slide 3: Scenarios
 | State | Redundancy in VNF | Failure detection | Use Case
VNF | Statefull | yes | VNF only | UC1
 |  |  | VNF & NFVI | UC2
 |  | no | VNF only | UC3
 |  |  | VNF & NFVI | UC4
 | Stateless | yes | VNF only | UC5
 |  |  | VNF & NFVI | UC6
 |  | no | VNF only | UC7
 |  |  | VNF & NFVI | UC8
UC9: Repeated failure in VNF

## Slide 4: UC1: Statefull VNF with Redundancy
NFVI
VM
VM
VM
VM
VNF
VNFM
STB
VIM
NFVO
ACT
NFVI’s Services
VNF’s
Services
NF
Failure detection: VNF only
ACT
1. VNFC fails
2. NF fails*
3. VNF detects the failure
4. VNF isolates VNFC
5. VNF fails over
6. NF recovers
7. VNF repairs VNFC
STB
Nothing new in this scenario
Recovery time
*Steps 1&2 are simultaneous they are separated for clarity

## Slide 5: UC1 Comments
SAL 1 can be achieved
The HA mechanism may be
  completely embedded in the VNF or
  exposed to the VNFM – requires additional communication toward the VNFM
In the VNF different error detection mechanisms can be used to detect the VNFC failure
  The assumption is that the fault causing the failure is in the VNFC
  If the VNFM manages the HA it needs to be in charge of the failure detection as well.

## Slide 6: UC2: Statefull VNF with Redundancy
NFVI
VM
VM
VM
VM
VNF
VNFM
STB
VIM
NFVO
ACT
NFVI’s Services
VNF’s
Services
NF
Failure detection: VNF & NFVI
ACT
1. VM fails
2. VM Service fails
5a. VNF detects the failure
5b. NFVI detects the failure
6a. VNF fails over
7a. NF recovers
11. VNF repairs VNFC
STB
3. VNFC fails
4. NF fails*
6b. NFVI reports to VIM
7b. VIM reports to VNFM
8. VNFM ok to VIM
9. VIM repairs VM
VM
10. VM Service recovers
Recovery time
*Steps 1-4 are simultaneous they are separated for clarity

## Slide 7: UC2 Comments
UC1 comments apply here except for 3.a.
The VNF and VNFM do not know the actual cause of the failure, which could be VM, host, hypervisor, networking etc. failure
  The VIM needs to resolve the cause
  The VNF likely to detect the failure through heartbeating via network
The VNF and NFVI may detect the failure in any order, which in turn determines the order and exchange of messages between the VNFM and VIM

## Slide 8: UC3: Statefull VNF with No Redundancy
NFVI
VM
VD
VM
VM
VNF
VNFM
VIM
NFVO
ACT
NFVI’s Services
VNF’s
Services
NF
Failure detection: VNF only
1. VNFC fails
2. NF fails*
3. VNF detects the failure
4. VNF isolates VNFC
5. VNF repairs VNFC
7. NF recovers
ACT
state
state
state
6. VNFC gets state
VNFC checkpoints its state to VD, which is HA
Recovery time
*Steps 1&2 are simultaneous they are separated for clarity

## Slide 9: UC3 Comments
The assumption is that the vDisk used by the VNFC is highly available meaning that
  Failures are handled by the NFVI transparently for the VNF
  The VNF have access to its state stored in the vDisk for at least 99.999% of the time
The VNFC’s availability management could be
  Embedded in the VNF or
  More likely: Done by the VNFM – requires additional communication between the VNF and VNFM see UC3-b

## Slide 10: UC3-b: Statefull VNF with No Redundancy
NFVI
VM
VD
VM
VM
VNF
VNFM
VIM
NFVO
ACT
NFVI’s Services
VNF’s
Services
NF
Failure detection: VNF only
1. VNFC fails
2. NF fails*
3. VNF detects the failure
6. VNFM repairs VNFC
8. NF recovers
ACT
state
state
state
7. VNFC gets state
VNFC checkpoints its state to VD, which is HA
Recovery time
4. VNF reports to VNFM
5. VNFM isolates VNFC
*Steps 1&2 are simultaneous they are separated for clarity

## Slide 11: UC4: Statefull VNF with No Redundancy
NFVI
VM
VD
VM
VM
VNF
VNFM
VIM
NFVO
ACT
NFVI’s Services
VNF’s
Services
NF
Failure detection: VNF & NFVI
3. VNFC fails
4. NF fails*
5a. VNF detects the failure
6a. VNF reports to VNFM
12. VNFM repairs VNFC
14. NF recovers
ACT
state
state
state
13. VNFC gets state
1. VM fails
2. VM Service fails
5b. NFVI detects the failure
6b. NFVI reports to VIM
7. VIM reports to VNFM
8. VNFM ok to VIM
9. VIM repairs VM
10. VM Service recovers
VM
Recovery time
VNFC checkpoints its state to VD, which is HA
11. VIM informs VNFM
*Steps 1-4 are simultaneous they are separated for clarity

## Slide 12: UC4 Comments
Comments of UC3 apply
Considering the time needed to repair the VM the target SALs cannot be met without the introduction of some redundancy
The VNF(M) does not know the actual cause of the failure, which could be VM, host, hypervisor, networking etc. failure. The VIM needs to resolve the cause
The VNFM and NFVI may detect the failure in any order, which in turn determines the order and exchange of messages between the VNFM and VIM

## Slide 13: UC5: Stateless VNF with Redundancy
NFVI
VM
VM
VM
VM
VNF
VNFM
Spare
VIM
NFVO
ACT
NFVI’s Services
VNF’s
Services
NF
Failure detection: VNF only
ACT
1. VNFC fails
2. NF fails*
3. VNF detects the failure
4. VNF isolates VNFC
5. VNF fails over
6. NF recovers
7. VNF restores redundancy
Spare
Nothing new in this scenario
Spare VNFC may or may not be instantiated
Recovery time
*Steps 1&2 are simultaneous they are separated for clarity

## Slide 14: UC6: Stateless VNF with Redundancy
NFVI
VM
VM
VM
VM
VNF
VNFM
Spare
VIM
NFVO
ACT
NFVI’s Services
VNF’s
Services
NF
Failure detection: VNF & NFVI
ACT
1. VM fails
2. VM Service fails
5a. VNF detects the failure
5b. NFVI detects the failure
6a. VNF fails over
7a. NF recovers
11. VNF restores redundancy
Spare
3. VNFC fails
4. NF fails*
6b. NFVI reports to VIM
7b. VIM reports to VNFM
8. VNFM ok to VIM
9. VIM repairs VM
VM
10. VM Service recovers
Spare VNFC may or may not be instantiated
Recovery time
*Steps 1-4 are simultaneous they are separated for clarity

## Slide 15: UC5 & UC6 Comments
Comments are similar to UC1 & UC2

## Slide 16: UC7: Stateless VNF with No Redundancy
NFVI
VM
VD
VM
VM
VNF
VNFM
VIM
NFVO
ACT
NFVI’s Services
VNF’s
Services
NF
Failure detection: VNF only
1. VNFC fails
2. NF fails*
3. VNF detects the failure
5. VNF isolates VNFC
6. VNF repairs VNFC
7. NF recovers
ACT
Recovery time
4. VNF reports to VNFM
*Steps 1&2 are simultaneous they are separated for clarity

## Slide 17: UC8: Stateless VNF with No Redundancy
NFVI
VM
VD
VM
VM
VNF
VNFM
VIM
NFVO
ACT
NFVI’s Services
VNF’s
Services
NF
Failure detection: VNF & NFVI
3. VNFC fails
4. NF fails*
5a. VNF detects the failure
6a. VNF reports to VNFM
12. VNF repairs VNFC
13. NF recovers
ACT
1. VM fails
2. VM Service fails
5b. NFVI detects the failure
6b. NFVI reports to VIM
7. VIM reports to VNFM
8. VNFM ok to VIM
9. VIM repairs VM
10. VM Service recovers
VM
Recovery time
11. VIM informs VNFM
*Steps 1-4 are simultaneous they are separated for clarity

## Slide 18: UC7 & UC8 Comments
In UC7 the HA mechanism may be embedded in the VNF or VNFM needs to provide it including the failure detection
In addition for UC8 the comments are similar to UC4
  Most importantly the target SALs cannot be achieved in case of UC8 without redundancy

## Slide 19: UC9: Stateless VNF with No Redundancy
NFVI
VM
VD
VM
VM
VNF
VNFM
VIM
NFVO
ACT
NFVI’s Services
VNF’s
Services
NF
Failure detection: VNF only – BUT Repeatedly
1. VNFC fails
2. NF fails
3. VNF detects the failure
and counts
4. VNF isolates VNFC
5. VNF repairs VNFC
6. NF recovers
ACT
1
…. VNFC fails….2
…. VNFC fails….3
…. VNFC fails….4
2
3
4
Fault is not in the VNFC!
ACT
ACT
UC7

## Slide 20: UC9: Stateless VNF with No Redundancy
NFVI
VM
VD
VM
VM
VNF
VNFM
VIM
NFVO
NFVI’s Services
VNF’s
Services
NF
Failure detection: VNF only – BUT Repeatedly
1. VNFC fails
2. NF fails
3. VNF detects the failure
and counts
4. VNF isolates VNFC
5. VNF repairs VNFC
6. NF recovers
ACT
…. VNFC fails….2
…. VNFC fails….3
…. VNFC fails….4
4
N. VNF reports to VNFM
N+5. VNF repairs VNFC
N+6. NF recovers
N+1. VNFM reports to VIM
N+2. VIM isolates VM
N+4. VM Service recovers
N+3. VIM repairs VM
VM

## Slide 21: UC9 Comments
Repeated failure at the VNF level within a short period of time typically indicate that the fault is not at the VNF level, it only manifesting there.
This applies to any of the cases when the failure is detected at the VNF level only
Faults in the HW, host OS, hypervisor may propagate to the tenant VMs in such a way that only the tenant can detect it
VIM is the only entity that knows the relation between the physical and virtual resources and can correlated these failures observed in one or more tenants

## Slide 22: To Be Considered
HA of the VD
  Different redundancy schemas
HA of the Network
  Switches and routers
Correlation of failures
  Failure of multiple VMs in the same host
  Different types of failures (i.e. compute, storage…)