## Slide 1: IPv6-enabled OPNFV
Bin Hu
IPv6 Project Lead, OPNFV
Other contributors of presentation
Henry Gessau, Sridhar Gaddam and Ian Wells

## Slide 2: Agenda
Key Project Facts
Goals and Deliverables
Status Quo of IPv6 in OpenStack
Use Case and Gap Analysis
Proof-of-Concept (PoC)
Next Steps

## Slide 3: Key Project Facts
Project Creation Date: November 25th, 2014
Lifecycle State: Incubation
Gerrit Repo: ipv6
Project Wiki: https://wiki.opnfv.org/ipv6_opnfv_project
Project Lead: Bin Hu bh526r@att.com
Primary Contact: Bin Hu bh526r@att.com
Seven committers from AT&T, Brocade, Cisco, ClearPath, Huawei and Nokia

## Slide 4: Goals and Deliverables
Goals
  A meta distribution of IPv6-enabled OPNFV platform
  A methodology of evolving IPv6 OPNFV
Deliverables
  An integrated package consisting of basic upstream components
  Auto configuration script to automate the configuration and provisioning of IPv6 features (for those that can be automated)
  An Installation Guide and/or User Guide with step-by-step instructions of manual configuration of IPv6 features (for those that cannot be automated)
  Test cases adapted to IPv6 specific use cases
  Gap analysis and Recommendation for next steps

## Slide 5: Status of IPv6 in OpenStack
Current Work (for Kilo release)
  Prefix Delegation integrated with IPAM
  Multiple Prefixes on ports and gateways
  IPv6 Router to support external connectivity
  Extra DHCP Options to validate option name, value and version before applying DHCPv4 or DHCPv6 address
  Stabilizing the existing IPv6 use cases, e.g. SLAAC, DHCPv6 Stateless and Stateful
Roadmap (after Kilo)
  Support L3 HA and Distributed Virtual Routers
Potential Future Work
  IPv6 only cloud in an dual-stack environment

## Slide 6: Multiple Prefixes in OpenStack
New Neutron capability for Kilo release
http://specs.openstack.org/openstack/neutron-specs/specs/kilo/multiple-ipv6-prefixes.html
Include SLAAC addresses implicitly on ports if subnet is IPv6
Dual-Stack Gateway Ports on Neutron Routers
Multiple IPv6 prefixes on internal router ports

## Slide 7: Prefix Delegation for OpenStack
New Neutron capability for Kilo release
http://specs.openstack.org/openstack/neutron-specs/specs/kilo/ipv6-prefix-delegation.html
Automatic prefix when creating IPv6 subnet
Neutron runs PD clients to get prefixes from an external PD server
Integrates with Neutron IP address management (IPAM)

## Slide 8: IPv6 Router in OpenStack
New Neutron capability for Kilo release
http://specs.openstack.org/openstack/neutron-specs/specs/kilo/ipv6-router.html
Simple change to enable external connectivity
Operator can configure external gateway
Neutron installs a default route with next hop being the gateway

## Slide 9: Use Case and Gap Analysis
Roadmap for Kilo Neutron
  IPv6 Router Support and code review
  Multiple IPv6 Prefixes and code review
  IPv6 Prefix Delegation and code review
Not considered in Neutron
  The ability to support non-DHCP statically assigned IPv6 addresses in the same fashion as is supported for IPv4
  Additional IPv6 extensions such as IPSec, IPv6 Anycast, Multicast etc. are not supported
  Access to metadata server (and GRE/VXLAN) still requires IPv4
  Floating IPv6 is rejected
IPv6 in ODL
  To be investigated

## Slide 10: Use Case and Gap Analysis – Topology
Requirement | Supported in Juno / Neutron? | Notes
All topologies work in a multi-tenant environment | Yes | The tenant's subnets are based on Neutron, with ML2 plugin and Single Flat Network topology, dual-stacked. Refer to Blueprints DHCPv6 and IPv6 SLAAC
IPv6 VM to VM only | Yes | Configuration and IPv6 address assignment
IPv6 external L2 VLAN directly attached to a VM | Yes | Refer to Provider Networking – Upstream SLAAC Support
IPv6 subnet routed via L3 agent to an external IPv6 network Both VLAN and overlay (e.g. GRE, VXLAN) subnet attached to VMs Must be able to support multiple L3 agents for a given external network to support scaling (neutron scheduler to assign vrouters to the L3 agents) | Roadmap Yes | Refer to Kilo Blueprints IPv6 Router Support and Multiple IPv6 Prefixes Scalability is supported. Patches for HA are under review
Ability for a VM to support a mix of multiple IPv4 and IPv6 networks Across the mix of all the above topologies including multiples of the same type | Yes Roadmap | Dual-stack is supported via Single Flat Network topology. Refer to Kilo Blueprints Multiple IPv6 Prefixes

## Slide 11: Use Case and Gap Analysis – Address Management and Translation
Requirement | Supported in Juno Neutron? | Notes
Support DHCP stateful Including the ability for a user to create a port on a IPv6 subnet and assign a specific IPv6 address to the port and have it taken out the DHCP address pool. Support the ability to assign multiple IPv6 address to an interface | Yes Work-in-progress | Refer to Patch 1 and Patch 2 Work-in-progress and expected in Kilo release. Full support of all the IPv6 configuration modes such as SLAAC, DHCPv6 Stateless and DHCPv6 Stateful are expected in Kilo release. Refer to Kilo Blueprint
Should not prevent the ability to support non-DHCP statically assigned IPv6 addresses in the same fashion as is supported for IPv4 | No | Sridhar is investigating more details
Support for private IPv6 to external IPv6 Floating IP | Rejected | Refer to discussion of Blueprint “Support Floating IP for IPv6”

## Slide 12: Use Case and Gap Analysis – Miscellaneous Protocols, Metadata Server and Security Groups
Requirement | Supported in Juno / Neutron? | Notes
Provide IPv6/IPv4 feature parity in support for pass-through capabilities (e.g. SR-IOV support in openstack) as these features are provided in openstack | Roadmap | Blueprint “Managing InfiniBand SR-IOV” is pending approval, “Traffic Rate Support for SR-IOV NIC” is being drafted, and “HA SR-IOV Ports” has not started yet.
Additional IPv6 extensions, for example: IPSEC IPv6 Anycast Multicast | No | It doesn’t appear to be considered yet
Access to the meta-data server to obtain user data and ssh keys etc. (may need more of a discussion) | No | Metadata (and GRE / VXLAN subnet) still requires IPv4. An alternate mechanism is to use config-drive. Refer to email thread.
Full support for IPv6 tcp/udp/icmp IPv6 security groups (same as we see for IPv4) | Yes | Response to Blueprint “Support ICMP type filter by security group” indicates that it is supported. Need to further lookinto Blueprint “Security group rule for IPv6 RA guard and IPv6 Snooping” which has not started

## Slide 13: Use Case and Gap Analysis – UI & CLI
Requirement | Supported in Juno Neutron? | Notes
During network/subnet/router create have the option to allow user to specify the type of address management they would like This includes all options including those low priority if implemented (e.g. toggle on/off router and address prefix advertisements) Must be supported via Neutron API (restful and CLI) as well as via Horizon | Yes Roadmap | The ability to create various types of IPv6 subnets (i.e., SLAAC / DHCPv6 Stateless / Stateful) is supported both using Neutron router and external router. Refer to various combinations and how to configure Neutron subnets. Refer to Blueprints “IPv6 Prefix Delegation” and “Multiple IPv6 Prefixes” for support of multiple IPv4 and IPv6 networks
Ability to specify Floating IPs via Neutron API (restful and CLI) as well as via Horizon Including combination of IPv6/IPv4 and IPv4/IPv6 Floating IPs if implemented | No | Floating IP support is rejected. Refer to discussion of Blueprint “Support Floating IP for IPv6”
Ability to control and manage all IPv6 security group capabilities via Neutron/Nova API (restful and CLI) as well as via Horizon | Yes | Related to Blueprint “Support ICMP type filter by security group” which indicates that it is supported

## Slide 14: Proof-of-Concept (PoC)
Objectives of PoC
  Explore the auto configuration and provisioning of existing IPv6 features
    OPNFV infrastructure nodes should be able to communicate with each other using IPv6
      VM-2-VM, SLAAC and DHCPv6 (stateful and stateless)
    OPNFV should be able to instantiate IPv6-enabled VMs in a multi-tenant environment
    OPNFV VMs should be able to connect with external IPv6 networks
      IPv6 external L2 VLAN directly attached to VM
      IPv6 subnet routed via L3 agent to an external IPv6 network
    Dual-stack should be supported
  Explore roadmap items
    Both IPv6 VLAN and overlay subnet attached to VMs
    Ability for a VM to support a mix of multiple IPv4 and IPv6 networks
    Ability to assign multiple IPv6 address to an interface
Work in Progress of PoC design
  A network topology is needed
    Provider network and tenant network
  Design the network architecture of the PoC

## Slide 15: Next Steps
Complete PoC design and implementation
Test case development
Verify gap analysis through PoC and Test
Complete easy installation package
  Based on Bootstrap deliverables components
  Automated script
  Installation Guide
Recommendation of filling the gap

## Slide 16: IPv6-enabled OPNFV
Thank you