## Slide 1
NFV/SDN Information and Data Models in Standards and Open Source
7 March 2016
Bryan Sullivan, AT&T

## Slide 2: OPNFV’s Role and Needs for Models
OPNFV integrates upstream projects into a coherent platform for NFV, starting from the infrastructure layer and moving up the management stack
OPNFV does not have an information model nor plans to establish one
  Relies on existing running code and data models from OpenStack, ODL, etc
OPNFV relies upon upstream open source projects / components which
  Expose/consume data via open APIs and specific adapters/translators
  Have implicit models, but not maintained in formal modeling language
  Are intended to have limited scope, yet sometimes compete, and evolve toward cleaner boundaries and model convergence over several releases

## Slide 3: Example: Lineage of standards adoption for TOSCA
2013 - OASIS TOSCA
- Focused on describing cloud services
- Large participation from cloud players
2014 – ETSI NFV ISG MANO
Non Normative specification for management and orchestration for NFV
2015 - TOSCA For NFV Profile
Based on the MANO VNF Descriptor
Evolving
2015 – NFV IFA
Several normative interface specs re Management and Orchestration, and NFV Information Modeling
TACKER
(Generic VNF Manager for OpenStack)
Note: example only; OPNFV has not yet selected/integrated VNFM solutions
Implementation feedback to published and in-progress specs (a goal…)
One example of how open source projects pick up draft specs, implement them and (can) provide feedback implementation experience to SDOs, as specs are developed or afterward

## Slide 4: Recommendations for the SDO Community
OPNFV as CATALYST
Accommodate REALITY
TIMELY publication
MODULAR design
Platforms
Standards
Customer
Motivation
Choice
Realization
Services
OPNFV
Open Source

## Slide 5: RFC 3444 on Information vs Data Models
Information Models:
  model “things” and “relationships” conceptually, in a protocol or implementation independent language
  focus on relationships between entities
  often represented using UML class diagrams
  no set rule for detail level or specificity; it depends on the needs of the designers
Data Models:
  a lower level of abstraction, with many details including attributes, constraints
  intended for implementers; include implementation and protocol-specific constructs
  often represented in formal data definition languages specific to management protocols

## Slide 6: Example: MEF’s LSO Management View Abstractions
Service View
Element & Equipment
Element Control & Management
Service Orchestration & Infrastructure Management
(Subnetwork)
LSO RA
Context
Information Class Examples per Management Abstraction View
Network Element
Card
Product
Offering
Endpoint
Logical Termination Point
Forwarding Construct
Port
Service Orchestration
(Provider domains & multi-domain)
Business Apps
Product View
Product
Catalog
Customer
Link
Network & Topology
Service
Server
Facility
Fabric
Management
Abstractions
Service Spec
Forwarding Domain
VNF
Resource View
Product
Spec
Product
Instance
Service Component
Service Access Point
Route
Link End
Cross Connect
VNE
Service
Interface
From NFV(16)000018_MEF_Modeling_Activities.pptx

## Slide 7: Dimensions(views) and perspectives
Views
  address complexity, provide clarity to stakeholders e.g. business, developer, system administrators
  A 4+1 view is typical
Perspectives
  Capture ways to describe a system
    Structural
    Functional
    Behavioral(Process)
    Rule
Scenarios
Logical
Development
Physical
Process

## Slide 8: Why do we need an Info Model?
Produce interface specifications for system components
Provide semantic alignment
  “What is a service?”
Enable declarative abstraction of application intent
  Simplify developer experience, e.g. application portability and maintenance
  Provide service providers with flexibility in how needs are fulfilled
Allow for translation between different data models
Execution Environment
Catalog
Editors

## Slide 9: Modeling in NFV
NFV is a complex, brownfield undertaking
VIM focus (cloud, SDN) leads to distinct modeling tools (Tosca, Yang)
Each tool is addressing somewhat the same problem domain
  Resources, configuration, and lifecycle management
There’s no time to wait for top-down harmonizing/aligning
  VNFs that have to be model-driven are being rapidly deployed
We must use what open source VIMs support today
We must also be prepared for it to evolve rapidly

## Slide 10: NFV need for models
Templates – metadata describing
  Resource requirements, VNF config parameters, design constraints
  Lifecycle event handling
  Examples
    OASIS TOSCA Simple Profile for NFV
    IETF L3VPN Service Model
Logical Models – required for interface specifications

## Slide 11: Open Source and Data Models
Open source software operates at the implementation level
Info models are usually not formally defined
Data models may be defined, or need inference from APIs and messages passed between software components
In OPNFV, the recently created Models project will
  Promote SDO-OpenSource collaboration on Info and Data Models
  Assess defined/derived model support in OPNFV upstream components
  Develop model-driven VNF use cases for testing on OPNFV releases
  Work with other projects to drive upstream blueprints as needed

## Slide 12: Open Source Model Support
Tosca | Yang
OpenStack: Heat-translator Tosca-parser Tacker (VNFD, more blueprints) Murano (Mitaka) App-catalog (blueprint) | OpenDaylight: Controller MD-SAL Yangtools YangIDE
XOS (e.g. samples) | YangForge (see L3VPN demo)
Cloudify (e.g. Clearwater IMS demo) | ONOS (proposed, based upon YangForge)
JuJu | OpenContrail (future… currently IF-MAP)
OpenTosca | Pyang (validator/converter)

## Slide 13: Demo!

## Slide 14: Come collaborate with us in OPNFV!