## Slide 1: Contrail Virtual Networking
Quick Tutorial
OpenContrail
quick Tutorial
Notes: We live in a connected world and the foundation for these connections is the network.
Broadband Internet traffic is doubling each and every year (according to IDC) [or] Internet traffic worldwide will grow three-fold by the year 2017. (Internet Trends, Mary Meeker (KCPB)
Today we have 2.5 billion Internet users in the world – roughly one-third of the Earth’s population. In the next decade, the number of Internet users will double to 5 billion (Mary Meeker, KPCB)
That means that two-thirds of the world will be connected by 2023.
When you add in the big trends of cloud, mobility, video and security, the combined rate of acceleration is placing unprecedented demands on the network.
[Optional stats/factoids]
100 hours of video uploaded every single minute to YouTube (YouTube)
Mobile video traffic exceeded 50 percent for the first time in 2012. (Cisco VNI)
Mobile network connection speeds more than doubled in 2012. (Cisco VNI)
In 2012, a fourth-generation (4G) connection generated 19 times more traffic on average than a non-4G connection. Although 4G connections represent only 0.9 percent of mobile connections today, they already account for 14 percent of mobile data traffic. (Cisco VNI)
[NOTE: Consider finding alternate source for above stats to avoid siting Cisco]
As you just described (refer to pain points from previous slide), you are living in this world and feeling the pressure every day.
Pradeep Sindhu founded Juniper 17 years ago on the belief that we should solve technology problems that matter most to our customers and that make a difference in the world. He recognized the importance of the network and the impact it would have on our world.
Our mission is simple, but powerful; to connect everything and empower everyone.
In today’s connected world, this mission is more relevant than ever.
Here at Juniper we are focused on helping alleviate those pain points through our portfolio of high performance networking products.
[T] And we do this by listening to our customers and helping them address their challenges and capitalize on their opportunities.

## Slide 2: Network/Cloud Technology interchange
Networking
Cloud Benefits
Software-defined networking
Network scale
Security
Resilience
Network Benefits
Service agility
Self-service
On-demand
Elastic scaling
Technology interchange benefits cloud and networks
Network Technology
Overlay networking (MPLS/VXLAN)
Control plane (BGP)
Network load balancing (ECMP)
Cloud
Cloud Technology
Common x86 platform
Shared service infrastructure
Service automation

## Slide 3: Contrail Virtual Networking
Quick Tutorial
How Contrail Works
Notes: We live in a connected world and the foundation for these connections is the network.
Broadband Internet traffic is doubling each and every year (according to IDC) [or] Internet traffic worldwide will grow three-fold by the year 2017. (Internet Trends, Mary Meeker (KCPB)
Today we have 2.5 billion Internet users in the world – roughly one-third of the Earth’s population. In the next decade, the number of Internet users will double to 5 billion (Mary Meeker, KPCB)
That means that two-thirds of the world will be connected by 2023.
When you add in the big trends of cloud, mobility, video and security, the combined rate of acceleration is placing unprecedented demands on the network.
[Optional stats/factoids]
100 hours of video uploaded every single minute to YouTube (YouTube)
Mobile video traffic exceeded 50 percent for the first time in 2012. (Cisco VNI)
Mobile network connection speeds more than doubled in 2012. (Cisco VNI)
In 2012, a fourth-generation (4G) connection generated 19 times more traffic on average than a non-4G connection. Although 4G connections represent only 0.9 percent of mobile connections today, they already account for 14 percent of mobile data traffic. (Cisco VNI)
[NOTE: Consider finding alternate source for above stats to avoid siting Cisco]
As you just described (refer to pain points from previous slide), you are living in this world and feeling the pressure every day.
Pradeep Sindhu founded Juniper 17 years ago on the belief that we should solve technology problems that matter most to our customers and that make a difference in the world. He recognized the importance of the network and the impact it would have on our world.
Our mission is simple, but powerful; to connect everything and empower everyone.
In today’s connected world, this mission is more relevant than ever.
Here at Juniper we are focused on helping alleviate those pain points through our portfolio of high performance networking products.
[T] And we do this by listening to our customers and helping them address their challenges and capitalize on their opportunities.

## Slide 4: contrail - based on mpls VPN technology
VM
Hypervisor with vRouter
Server
Tenant VRF
Encapsulation Tunnel
XMPP (BGP)
Datacenter
Route Reflector
BGP
Provider Network
L3 VPNs for Inter-Site Connectivity Traffic segmentation in the WAN MPLS over MPLS label encapsulation tunnels BGP route signaling
Contrail Virtual Networks in Datacenters Traffic segmentation in the LAN MPLS over GRE or VXLAN label encapsulation tunnels XMPP (with BGP payload) route signaling
Protocols, Architecture
Customer Site
CE Router
PE Router
Customer VRF
Encapsulation Tunnel
OpenStack Cloud Manager
Contrail Controller

## Slide 5
Underlay Switch
vRouter
Control Node
Control Node
Underlay Switch
vRouter
VM
VM
IBGP
XMPP
MPLS over GRE or VXLAN
Config Node
OpenStack
Analytics Node
SDN System
Contrail
P
P
PE
PE
Route Reflector
Route Reflector
CE
CE
IBGP
IBGP
MPLS over MPLS
Network Management System (NMS)
DMI
MPLS L3VPN / E-VPN
Gateway
BGP

## Slide 6: Contrail Abstraction Architecture
Orchestration, Automation Open source and partner ecosystem of orchestrators
API and SDK for integration with OSS / BSS
OSS
Virtual Network Overlay
Overlay encapsulation implemented in hypervisor
Multi-tenancy for private and virtual public clouds
Gateway functions - connect to virtual to physical network
Service chaining (physical and virtual)
Physical Network
Interoperability with traditional network devices
Any-to-any non-blocking low-latency fabric: Q-Fabric or Clos
Control Plane - Physical, Virtual
Open, standards-based, federated controller
Scalable and resilient
Control Plane
Configuration model
Automation
Control Plane
Control Plane
Policies and requests
Analytics
Distributed collection
Global view
Consolidation
Aggregation
State and status

## Slide 7: Contrail Components
Physical Network (no changes)
Collector
OPENCONTRAIL CONTROLLER
Control
Configuration
Physical Host
with Hypervisor
vRouter
VM
VM
VM
VM
Physical Host
with Hypervisor
vRouter
VM
VM
VM
VM
WAN, Internet
Gateway
Accepts and converts orchestrator requests for VM creation, translates requests, and assigns network
Real-time analytics engine collects, stores and analyzes network elements
Interacts with network elements for VM network provisioning and ensures uptime
vRouter: Virtualized routing element handles localized control plane and forwarding plane work on the compute node
Gateway: MX Series (or other router) or EX9200 serve as gateway eliminating need for SW gateway & improving scale & performance

## Slide 8: Scale Out, Highly Available Architecture
Logically Centralized (Physically Distributed)
Horizontally Scalable
Highly Available
(Active-Active)
Federated
Configuration Nodes
Control
Nodes
Analytics Nodes
IF-MAP
REST
REST
XMPP
BGP
BGP, Netconf
vRouters
Gateways
BGP
Database Nodes
Web UI Nodes
https://github.com/Juniper/contrail-controller/wiki/Roles-Daemons-Ports
HTTP

## Slide 9: Compute Node – Hypervisor/Container with vRouter
Compute Node
Virtual Machine (Tenant B)
Virtual Machine (Tenant B)
vRouter Forwarding Plane
Virtual Machine (Tenant A)
Routing Instance (Network X)
Routing Instance (Network Y)
Routing Instance (Network Z)
vRouter Agent
Flow Table
FIB
Flow Table
FIB
Flow Table
FIB
Overlay tunnels MPLS over GRE or VXLAN
JUNOSV CONTRAIL CONTROLLER
CONTRAIL CONTROLLER
XMPP
Eth1
Kernel
pkt0
User
Eth0
EthN
Config
VRFs
Policy Table
Top of Rack Switch
XMPP
vRouter is replaces the Linux Bridge or OVS module in Hypervisor Kernel
vRouter performs bridging (E-VPN) and routing (L3VPN)
vRouter performs networking services like Security Policies, NAT, Multicast, Mirroring, and Load Balancing
No need for Service Nodes or L2/L3 Gateways for Routing, Broadcast/Multicast, NAT
Routes are automatically leaked into the VRF based on Policies
Support for Multiple Interfaces on the Virtual Machines
Support for Multiple Interfaces from Compute Node to the Switching Fabric
Tap Interfaces (vif)

## Slide 10: Contrail – control node
Control Plane Nodes federate using BGP
Each vRouter uses XMPP to connect with multiple Control Plane nodes for redundancy
All Control Plane Nodes are active active
Each Control Plane Node connects to multiple configuration nodes for redundancy
BGP is used to connect with Physical Gateway Routers or Services Nodes
Configuration Node
Configuration Node
IF-MAP
Compute Node
Compute Node
XMPP
Control Node
"BGP module"
Proxies (ARP, DHCP, ..)
XMPP
IF-MAP Client
IBGP
Service Node
Gateway Routers
Control Node Peers
BGP
Notes: Each vrouter agent connects to at least two control nodes. Both control nodes are active. The vrouter receives all state (routes, routing instance configuration, etc.) from both control nodes. The vrouter agent receives and stores both copies of the control state, one copy from each controller. The state received from the two controllers is guaranteed to be eventually consistent but may be transiently inconsistent. It makes a local decision about which copy of the control state to use. This is similar to how a BGP PE router receives multiple copies of the same route (one from each IBGP neighbor) and makes a local best route selection.
If a controller fails, the vrouter agent will notice that the connection to that controller is lost. The vrouter agent will flush all state from the failed controller. It already has a redundant copy of all the state from the other controller. The vrouter can locally and immediately switch over without any need for resynchronization. The vrouter agent will contact the service discovery server again to re-establish a connection with a new controller node to replace the failed controller node.

## Slide 11: configuration node
API Server provides Northbound REST Interface – Orchestration System provisions using this API service
DHT/NoSQL Database is used for Persistence and High Availability of Configuration
Schema Transformer “compiles” the high level data model to low level model for vRouter, Service Nodes, and Gateway Routers
IF-MAP is used to represent the data-model – Control Nodes subscribe to the subset of configuration
Configuration Node
REST API Server
Schema Transformer
Orchestrator (OpenStack)
REST
DHT DB
IF-MAP server
Control Node
Control Node
IF-MAP
Distributed Synchronization
Message Bus

## Slide 12: Interaction with OpenStack
OpenStack
Compute Node
Horizon
Compute Driver
Virtual-IF
Driver
Nova Compute
Contrail Agent
vRouter (kernel)
Virtual Router
Nova API
1
Create an Instance (Image, Network, …)
2
Nova Scheduler
Schedule an Instance on the Compute Node
Neutron Driver
3
VM Network Properties
4
Add Port
7
VM Interface config over XMPP
Scripts
Neutron Plugin
Configuration Node
Create VM Interface
5
6
Publish VM
i/f on IF-MAP
Control
Node

## Slide 13: Compute Node – DNS Resolution
VIRTUAL
PHYSICAL
Overlay tunnels MPLS over GRE or VXLAN
Compute Node
vRouter Forwarder
Virtual Machine (IP-VM1)
Routing Instance
Flow Table
FIB
Eth1 (IP-H1)
Tap Interfaces (vif)
Compute Node
vRouter Forwarder
Virtual Machine (IP-VM2)
Routing Instance
Flow Table
FIB
Eth1 (IP-H2)
Tap Interfaces (vif)
DNS – IP for VM2
OpenContrail
OpenStack

## Slide 14: Compute Node – proxy ARP
VIRTUAL
PHYSICAL
Overlay tunnels MPLS over GRE or VXLAN
Compute Node
vRouter Forwarder
Virtual Machine (IP-VM1)
Routing Instance
Flow Table
FIB
Eth1 (IP-H1)
Tap Interfaces (vif)
Compute Node
vRouter Forwarder
Virtual Machine (IP-VM2)
Routing Instance
Flow Table
FIB
Eth1 (IP-H2)
Tap Interfaces (vif)
ARP [Who is IP-VM2]

## Slide 15: Compute Node – Forwarding/Tunneling
VIRTUAL
PHYSICAL
Overlay tunnels MPLS over GRE or VXLAN
Compute Node
vRouter Forwarder
Virtual Machine (IP-VM1)
Routing Instance
Flow Table
FIB
Eth1 (IP-H1)
Tap Interfaces (vif)
Compute Node
vRouter Forwarder
Virtual Machine (IP-VM2)
Routing Instance
Flow Table
FIB
Eth1 (IP-H2)
Tap Interfaces (vif)
IP-VM2
Payload
Virtual-IP2
Payload
MPLS / VNI
IP-H2
IP-VM2
Payload
IP-VM2
Payload
MPLS / VNI
IP-H2

## Slide 16: FEATURE: DISTRIBUTED SECURITY POLICY
VIRTUAL NETWORK GREEN
Host + Hypervisor
Host + Hypervisor
VIRTUAL NETWORK BLUE
VIRTUAL NETWORK YELLOW
Contrail Security Policy
(Firewall-like e.g. allow only HTTP traffic)
Contrail Policy with a Firewall Service
IP fabric (switch underlay)
G1
G2
G3
B3
B1
B2
G1
G3
G2
Y1
Y2
Y3
B1
B2
B3
Y2
Y3
Y1
VM and virtualized Network function pool
Intra-network traffic
Inter-network traffic traversing a service
…
…
LOGICAL
(Centralized Policy Defn)
PHYSICAL
(Distrib. Policy Enforcement)
Non-HTTP traffic
Notes: The idea is that there is a logical or Policy definition layer and a separate physical or policy enforcement layer, and things look and feel different in these two layers. In the policy defnition layer, operator can specify policies like create 3 virtual networks Green, Blue and Yellow, such that any traffic from Blue virtual network to yellow virtual network will have to go through a scale-out Firewall service, and only allow port 80 traffic from green to Blue virtual network.

## Slide 17: FEDERATED DOMAINS UNIFIED CONTROL PLANE ACROSS PHYSICAL/VIRTUAL NETWORKS
Control Node
Control Node
…
Config Node
x86 Host + Hypervisor
x86 Host + Hypervisor
Underlay Switches
XMPP
BGP
MPLSoGRE, MPLSoUDP, VXLAN
vRouter
vRouter
BGP
Route Reflector
Route Reflector
…
BGP
BGP
PE
PE
PE
NMS
WAN Control/Mgmt
Orchestration, OSS/BSS
OpenContrail
Cloud Management
Public Network
CLOUD DC
IP / MPLS VPN

## Slide 18: FEATURE: SERVICE CHAINING
SVC 1 VM
SVC 2 VM
L4
L6
L3
L5
L3
R1
R2
L4
Srvr IP = S1
Server IP = S2
Srvr IP = S4
L5
L6
Srvr IP = S3
Locally significant MPLS Labels
Seamless insertion of Juniper & unmodified 3rd Party services using existing L3VPN connections
Allows multiple Services in a chain
Allows multiple service chains between virtual networks
Supports L3 services without the use of a gateway
RI for non-svc-chain traffic
LOGICAL
PHYSICAL
G1
G2
VIF 2
L2
Interf = VIF 1
Label = L1
VIF 4
L8
Interface = VIF 3 Label = L7
Dst | Next Hop
G1 | S2  L3
G2 | S2  L3
R1 | VIF 1
R2 | VIF 2
Dst | Next Hop
R1 | S1  L1
R2 | S1  L2
Dst | Next Hop
G1 | S3  L5
G2 | S3  L5
Dst | Next Hop
R1 | S2  L4
R2 | S2  L4
Dst | Next Hop
G1 | S4  L7
G2 | S4  L8
Dst | Next Hop
R1 | S3  L6
R2 | S3  L6
G1 | VIF 3
G2 | VIF 4
SVC 1 VM
SVC 2 VM
X86 Servers
Routing Instances
R1
R2
Virtual Network
Red
L2
L1
Virtual Network
Green
G1
G2
L7
L8
IP Fabric
For more details, see - https://datatracker.ietf.org/doc/draft-fm-bess-service-chaining/

## Slide 19: Service Virtualization and Chaining
Chain of virtual services
Chain of virtual services – independent scaling
DPI
DPI
DPI
DPI
DPI
DPI
DPI
DPI
Load balance between service layers
Stateful services require consistent forward/reverse paths
Decide which traffic goes into chain
NAT
Firewall
IDP
Cache
Anchor Router (Classifier)
NFV: Virtual Network Functions
Best in breed, from multiple vendors, including Juniper (e.g. vSRX)
SDN: Service Chaining
OpenContrail: Dynamically program network to create service chains
https://datatracker.ietf.org/doc/draft-fm-bess-service-chaining/

## Slide 20: FEATURE: ANALYTICS
Notes: Monitor Control Nodes
Monitor traffic stats per instance
Attach PCAP across VN’s – drill further in Wireshark
Execute SQL-like query for individual flows

## Slide 21: FEATURE: UNDERLAY-OVERLAY CORRELATION
Visual representation of topology (discovered using LLDP)
What underlay path are taken by flows (active or historical)
Delails of VMs, vRouters, and underlay components
Details of active flows
Ability to show historical flows as well

## Slide 22: CONTRAIL - KEY FEATURES
Routing & Switching
(IPv4, v6)
IPAM, DNS, DHCP
SNAT, FIP, QoS
Load Balancing
Security Policy Enf., Distributed FW
3rd Party Netw. Svc.
Gateway Services (L2, L3 GW)
Rich Analytics, Overlay-Underlay Correlation
Service Chaining
High Availability
API Services

## Slide 23: OpenContrail in OPNFV
OpenContrail is upstream to OPNFV
Working with installers for B release
  Fuel
  JOID
  Apex
  Compass4nfv
OpenContrail Sandbox on opencontrail.org
6 server POD almost ready for CI/test in NJ OpenLab

## Slide 24: OPENContrail OPENSOURCE APPROACH (For more info visit www.opencontrail.org)
OpenContrail Advisory Board (OCAB)
Industry veterans and key project users/adopters
Governance, Evangelism, Roadmap, Operational efficiency
Continuous Integration/Development
Features & Bug fixes
Single Github Source Code Repository
OpenContrail Community Release
Community Support
(Email, IRC, Forums)
Juniper Contrail Releases
Hardened for Production
Licensed Software
24x7 JTAC & Engineering
Bug Fix Release
Launchpad
Open Source (Users, Devs)
Bugs,
Design Blueprints
Customers
x
x
OpenContrail Developer Community
Majority Juniper, Some External developers
Proposing features & Contribute Code
Participate in Code review process
Community Release
Notes: Contrail as I mentioned is open sourced under Apache v2 license … There is a single source code repo on github with open bug database on Launchpad …
There are community releases – but Juniper monetizes through support …
Overseeing all of
More info @ opencontrail.org

## Slide 25: VNF Validation program for OpenContrail
Certification Tier | Basics | Functional Validation | Performance Benchmarks | Customizing and API Integration
Silver | ✓ |  |  | 
Gold | ✓ | ✓ |  | 
Platinum | ✓ | ✓ | ✓ | ✓
Launching in response to customer and VNF vendor interest

## Slide 26: CONTRAIL DEMO VIDEOS
DDoS Protection (Contrail + DDoS Secure)  http://www.youtube.com/watch?v=TnvCea4fil4
NFV through Contrail (this is the Internet / Firewall NFV aka. vCPE)  http://www.youtube.com/watch?v=_64no8P2vUw
Contrail - Elastic cloud - IT as a Service  http://www.youtube.com/watch?v=9g3EWV8X64s
SSLVPN on Contrail  http://www.youtube.com/watch?v=vfZfdH4kkV4
Caching as a Service (Junos Content Encore on Contrail  https://www.youtube.com/watch?v=-_NtC34wcRw
Hybrid Cloud  https://www.youtube.com/watch?v=uC7nMW5PXdg
USE CASE - DEMO VIDEOS
Bare Metal Integration through multi-vendor TOR integration  https://www.youtube.com/watch?v=PjkNt0yV3H0
IPv6 DVR (Distributed Virtual Router)  https://www.youtube.com/watch?v=RLO0uIXbDxo
OpenStack Neutron at Scale  https://www.youtube.com/watch?v=xN0rXHD_dqk
P + V Service Chaining  https://www.youtube.com/watch?v=a9HqC9x6KTg
Multi-hypervisor, Docker Integration  https://www.youtube.com/watch?v=x2n5Q_ycx6o
vRouter DPDK Demo  https://www.youtube.com/watch?v=ZGiQJrKoDQM
Physical + Overlay Correlation  https://www.youtube.com/watch?v=B8aHoY—1Zs
PRODUCT CAPABILTIIES - DEMO VIDEOS
Demo – Today. 1:25

## Slide 27: Thank You